## Slide 1: A Better Way to De-shelve 137Ba+
Andrea Katz
Trinity University
UW REU 2010

## Slide 2: Review of Quantum Computing
Traditional computers use bits, which can only be either 0 or 1.
Quantum computing employs qubits, which can be any linear combination of 0 and 1.
Quantum computers could quickly factor large numbers (Shor’s algorithm) and break RSA encryption

## Slide 3: How Do We Make a Qubit?
We can implement a qubit by allowing two energy levels in a trapped ion to be the two states of the qubit.
Paul traps:
http://depts.washington.edu/qcomp/pdfs/matt_thesis.pdf

## Slide 4: Ba+ as a Qubit
Simplified energy level diagram for 137Ba+

## Slide 5: Overview of my project
Produce an orange beam by sending an infrared laser beam through a PPLN waveguide
Align the orange beam and get it to the ion trap
Set up a double passed acousto-optic modulator and a Fabry-Perot cavity to help with laser stabilization

## Slide 6: Getting Orange from Infrared
IR Laser
AOM
Coupler
PPLN wave-guide
Polarization Paddles
To Cavity
To Ion

## Slide 7: PPLN Waveguides
PPLN (Periodically poled lithium niobate) crystals have a periodic reversal of domain orientation
Non-linearity of the crystal allows for second harmonic generation
PPLN crystals are more efficient than other non-linear crystals for second harmonic generation because of x2 nonlinearity
Using a waveguide instead of a regular crystal also increases SHG efficiency

## Slide 8: Phase Matching in PPLN
Phase matching is essential for efficient second harmonic generation!
We can adjust temperature to achieve phase matching.
http://www.thorlabs.com/catalogPages/693.pdf

## Slide 9: Fabry-Perot Cavities and Stabilization
Only certain wavelengths of light are resonant within the cavity, those in which an integer number of wavelengths fit inside the cavity.
We can “lock” the laser to the transmission peak closest to our desired wavelength.
http://www.int.washington.edu/REU/2009/2009_images/Adams_and_Davis.pdf

## Slide 10: Future Steps
Complete laser stabilization at the right wavelength
Use the orange beam to de-shelve 137Ba+!

## Slide 11: Thanks to Boris Blinov and the Trapped Ion Quantum Computing Group!
References:
Adams, Corey and Anya Davis. “Quantum Computing with Trapped Ions and Laser Cooling.” http://www.int.washington.edu/REU/2009/2009_images/Adams_and_Davis.pdf
Dietrich, M.R. Barium Ions for Quantum Computation. http://depts.washington.edu/qcomp/pdfs/matt_thesis.pdf
“Periodically Poled Lithium Niobate (PPLN)- Tutorial.” http://www.thorlabs.com/
catalogPages/693.pdf