## Slide 1: Simulating Radioactive Decays in Next Generation Geoneutrino Detectors
Megan Geen
Wheaton College
Advisor: Nikolai Tolich
August 17, 2011

## Slide 2: Introduction: The Earth’s Heat Production
Radius is ~6370 km
Continental crust is 30 km thick
Earth heat production:
  Geological sampling: 42 TW
  Estimates from radiogenic decay: 19 TW
Radiogenic decays from: 238U, 232Th, & 40K
Crust
Upper Mantle
Lower Mantle
Outer Core
Inner Core

## Slide 3: Introduction: Anti-Neutrinos (Geoneutrinos)
Anti-neutrinos are the antimatter counterpart to the neutrino
Comes in 3 flavors (electron, muon, tau)
Geoneutrinos are electron anti-neutrinos that come from interactions inside the Earth
Produced by
beta decay:
  n p + e- + νe

## Slide 4: Introduction: Anti-Neutrinos (Geoneutrinos)
Neutrinos are less reactive than other particles and can make it to the crust
Can be detected by
  inverse beta decay:
  νe + p e+ + n
Crust
Upper Mantle
Lower Mantle
Outer Core
Inner Core
νe
e+
α
n
time
light
200 μs

## Slide 5: Methods: Detector Design
Grid of NxN tubes
Each tube contains:
  Liquid Scintillator
  Acrylic Container
Photomultiplier
tube positioned
at each the end
of a tube
Optical dense acrylic and an air gap separates
each tube

## Slide 6: Methods: Detector Design
Liquid scintillator creates light from charged particles within the detector
The amount of light produced is proportional to the energy of the charged particle
Design takes advantage of total internal reflection

## Slide 7: Methods: Position Reconstruction
Position =
  Δt = difference in first photon arrival at each PMT
  c = speed of light in vacuum
  n = index of refraction of scintillator
  p0 = correction value
1
2
(Δt)( )( )
c
n
p0
1

## Slide 8: Methods: Energy Reconstruction
KE =
  charge = # of photons that hit the PMTs in a single tube
  u = p0 + p1(x2) +p2(x4) where x is the position
u
charge

## Slide 9: Methods: Energy Reconstruction
The reconstructed KE of a 1 MeV electron

## Slide 10: Methods: Particle Identification
Depending on the particle type, KE will be found in 1 or more tubes
Our particle ID =
Highest KE from all tubes
Total KE
Upper left has most KE = 1MeV
Total KE = 1MeV
ID = 1/1 = 1
Upper left has most KE = .5MeV
Total KE = 1MeV
ID = .5/1 = .5

## Slide 11: Methods: Coincidence Rate
# of Decays in 1 Year |  |  | 
 | 238U | 232Th | 40K
Gd Scintillator | 1.99x101 | 2.86x102 | 2.93x104
Acrylic | 1.77x105 | 5.76x104 | 7.65x109
Coincidence Rate is the # of decays that look like a geoneutrino:
Coincidence Rate
(Decay Rate) x (Neutron Detection Rate) x (Time Slice) x (# of Decays in the Chain) x (Efficiency)
=
Neutron Detection Rate: 10 (per second)
Time Slice: 1x10-3 seconds
Decays in a Chain: 238U=14 232Th=10 40K=1
  νe + p e+ + n

## Slide 12: Analysis & Results: Simulation Suite
Each simulation consisted of 100 decays of the same type spread out within the center tube
The decays only occur within either the acrylic or liquid scintillator
Decays included:
  Inverse beta
  Uranium
  Thorium
  Potassium

## Slide 13: Analysis & Results: Inverse Beta Decay
KE for an Inverse Beta Decay with Gd Scintillator

## Slide 14: Analysis & Results: Inverse Beta Decay
Positrons and neutrons are distinct in identification

## Slide 15: Analysis & Results: Inverse Beta Decay
Focus on the positron region

## Slide 16: Analysis & Results: All Decays
Black: β- , Blue: 238U , Red: 232Th , Green: 40K

## Slide 17: Analysis & Results: All Decays
Cut: 1MeV < KE < 3MeV & ID < .91

## Slide 18: Analysis & Results: Efficiencies
Efficiency |  |  |  | 
 | e+ | 238U | 232Th | 40K
Gd Scintillator | .98 | .0489 | .0741 | .05
Acrylic | .50 | .111 | .108 | .03
Efficiency =
# of Events Within Cut
Total # of Events
Coincidence Rate
(Decay Rate) x (Neutron Detection Rate) x (Time Slice) x (# of Decays in the Chain) x (Efficiency)
=

## Slide 19: Conclusions:
We expect to see ~50 geoneutrinos per year
Coincidence Rates in the scintillator is alright and problematic in the acrylic
Acrylic contains high concentrations of
238U, 232Th, & 40K
Can lower the neutron detection rate
Coincidence Rate in 1 Year with Efficiencies |  |  | 
 | 238U | 232Th | 40K
Gd Scintillator | 1.91 | 2.12x101 | 1.47x101
Acrylic | 3.11x106 | 5.36x105 | 2.29x106

## Slide 20: Future Work:
Better particle identification
  2nd or 3rd highest KE tubes
  Sum of KE in certain tubes
Different detector dimensions
  Various heights, widths, and depths
  1 tube made of multiple smaller tubes
More processes that can occur
  Interactions with Carbon
  Build up of certain isotopes in the decays chains

## Slide 21: Acknowledgments:
Advisor: Nikolai Tolich
Post-docs: Hok Seum Wan Chan Tseung & Jarek Kaspar
REU Coordinators: Alejandro Garcia & Deep Gupta
UW REU Program and the NSF