## Slide 1: Microwave Cavity Structures for an Axion Search
R.E.U. Presentation
August 13, 2012
Hunter Swan

## Slide 2: Meet Axion
Strong CP Problem: Why is QCD not CP violating?
Why is this parameter ≈ 0?
Peccei & Quinn (1977):
Promote θ to a field
As a field, θ tries to minimize itself to 0
Axions grow out of the new field
Axions with appropriate mass make possible dark matter candidate
a
γ
γ
LQCD = θ(E · B) + (other stuff)

## Slide 3: ADMX: Axion Dark Matter eXperiment
Sikivie Axion Detector:
Axions can interact with a strong B field to produce photons
If the cavity has the right shape, the photons interfere constructively, producing an appreciable electric field
“Right Shape” means:
  Mode frequencies near axion frequencies
  High “form factor” (roughly, ∫ E ⋅B dV is big)
a
B

## Slide 4: A “Fine Tuning Problem”
Tuning the cavity’s modes is critical, since the axion mass is unknown
To tune the frequency upwards, copper tuning rods are used
To tune frequency down, use dielectric rods instead of copper
  Can hurt form factor
  Dielectrics lossy, expensive

## Slide 5: Idea: Slow Wave Analogy
“Slow wave structures” used widely in waveguides to accommodate longer wavelengths
  Works for TE modes, not TM
Inspiration: add “slow wave structure” to cavity end plates
γ
γ

## Slide 6: Before
E
E
After
&

## Slide 7: Poisson/Superfish “My Hero”
Program to model cylindrically symmetric cavities
  Finds frequencies and field patterns of cavity modes

## Slide 8: Superfish Predicts Success
Chart: Frequency of lowest mode vs. depth of ridges (ADMX sized cavity - 1 m tall, .5 m diameter)
| 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 | 21 | 23 | 25
 | 457.992 | 453.468 | 443.876 | 426.943 | 402.913 | 375.303 | 347.688 | 321.959 | 298.745 | 278.053 | 259.684 | 243.344 | 228.745
 | 456.97 | 448.437 | 432.745 | 409.952 | 383.091 | 355.641 | 329.657 | 305.975 | 284.733 | 265.781 | 248.89 | 233.784 | 220.213
 | 459.351 | 458.051 | 453.53 | 443.75 | 426.046 | 400.721 | 372.049 | 343.939 | 318.134 | 295.049 | 274.613 | 256.522 | 240.459
 | 456.475 | 447.318 | 431.18 | 408.208 | 381.426 | 354.165 | 328.396 | 304.899 | 283.813 | 264.991 | 248.202 | 233.179 | 219.67
 | 455.905 | 446.139 | 430.442 | 408.764 | 383.294 | 356.848 | 331.465 | 308.026 | 286.83 | 267.821 | 250.816 | 235.575 | 221.845
 | 457.404 | 452.203 | 443.803 | 430.693 | 411.667 | 387.612 | 361.339 | 335.465 | 311.4 | 289.597 | 270.111 | 252.726 | 237.19
 | 456.76 | 447.273 | 431.125 | 408.742 | 382.702 | 355.955 | 330.454 | 307.017 | 285.875 | 266.939 | 250.011 | 234.843 | 221.185
 | 457.1 | 449.784 | 437.877 | 420.623 | 398.444 | 373.384 | 347.824 | 323.401 | 300.897 | 280.525 | 262.239 | 245.843 | 231.107
 | 457.341 | 449.719 | 437.323 | 419.477 | 396.814 | 371.543 | 346 | 321.696 | 299.353 | 279.147 | 261.013 | 244.752 | 230.127

## Slide 9: Factoring in the Form Factor
Chart: Form factor vs. frequency
Form factor depended more strongly on ridge configuration than did the frequency
Led to choosing the geometric configuration shown for further testing

## Slide 12: Instructions: Insert antennas into microwave cavity for 30 seconds, or until done.
Antenna Probes
Vin
Vout
Network
Analyzer
Log|Vin/Vout|
(Transmission)
γ

## Slide 14
Chart: Ridged Cavity's Transmission vs. Frequency
Predicted Mode Frequencies | -19 | -19 | -20 | -42.5 | -20 | -20 | -10 | -10 | -10 | -10 | -10 | -10

## Slide 15: Q: What is the Q?
A: ≈ 17000 (flat end plates); ≈ 3600 (with ridges)
  Quality factor is of expected magnitude
Chart: Frequency
Δf
Q = f/Δf ≈ 17000
f

## Slide 16: Results
Frequency shift | 
Form factor | 
Q | 
Success | 

## Slide 17: Cavity of the Future
Many more geometries worth investigating
  Frequency, form factor should be optimized
Incorporate into ADMX?

## Slide 18: Thanks
Professor Rosenberg, Gray Rybka, Andrew Wagner, Christian Boutan, & Dima Lyapustin—the ADMX fellows.
Deep Gupta, Alejandro Garcia, Janine Nemerever, & Linda Vilett—the REU folks.
Emma, Becca, Emily, Rachel, Eli, Jarrett, & Scott—they’re cool people.
God—your great, and you got me through this presentation.

## Slide 19: Disclaimer
The opinions expressed in this presentation are solely the work of those presenting them and do not necessarily reflect the views of ADMX or any of its collaborators, funding agencies, or affiliates. ADMX is not liable for any damage, injury, or ill will that may come about as a result of this presentation or any material contained therein.